## Slide 1: CFD Analysis of a Super Sonic Nozzle
By Max Plomer

## Slide 2: Problem Specification
Air flows at a high speed through a circular cross-section, custom designed converging-diverging nozzle
Air at inlet is atmospheric: 101,325 Pa and 300K
Outlet conditions are 3000 Pa and 300K
Large Reynolds number, viscous effects will be small, therefore flow modeled as invicid

## Slide 3: Initial Arbitrary Nozzle Design
L = 0.5 m
r = 0.15m
r = 0.1m
Need an equation for the line of form: Y= A*X2 + B
With points (0 , 0.1) and (0.25 , 0.15)
Therefore: Y= 0.8*X2 + 0.1
Increase the outlet radius up until r = 0.3m to see how the mach number at the wall and axis is affected.

## Slide 4: Why Varying Outlet Area?
Rocket engines use a converging-diverging nozzle, and an increase in the area of the outlet gives a higher mach # at the exit, but limits the range of back pressures that the rocket can operate.
With a correct integration of the chemistry for methane or hydrogen, an engineer can design their rocket to be most efficient for all the back pressures of the application.

## Slide 5: 2-D Mesh
Since Axi-symmetric, modeled top half only
Used a 40x100 mesh
Set boundary types as: Pressure-inlet, Pressure-outlet, Wall & Axis

## Slide 6: Fluent Physics Options
Solver: Since we have a high-speed compressible flow, using the density-based solver
Space: Solve the axi-symmetric form of the governing equations
Viscous Model: Inviscid, solver will neglect viscous terms
Using Energy Equation, because since a compressible flow, energy equation will be coupled to continuity and momentum equations
Density of Air: Ideal gas
Pressure inlet: 101,325 Pa @ 300K, Pressure outlet: 3,000 Pa@300K
Solution Methods: Second Order Upwind
Convergence criteria for : 1*10-6
600 Iterations

## Slide 7: Convergence
For the given mesh & parameters simulation converges at around 500 iterations

## Slide 8: Results – Velocity Contour (Mach #)
Notice: velocity greater at wall for diverging section

## Slide 9: Results – Velocity X-Y Plot
Axis reaches mach 2.05, while Wall reaches mach 2.55

## Slide 10: Results – Static Pressure (Pa)
Notice that pressure decreases from left to right

## Slide 11: Results – Total Pressure
Notice pressure loss at outlet, due to false diffusion

## Slide 12: Results – Static Temperature (K)

## Slide 13: Results – Total Temperature (K)
Notice the constant total Temp of 300K, and round off error near the outlet

## Slide 14: Varying of Outlet Radius, to see effect on Mach #
Running simulations for Routlet = 0.15m, 0.20m, 0.25m & 0.30m, with all other parameters the same.
Equation for points left of origin still Y= 0.8*X2 + 0.1
For right of origin equations are:
0.15m: Y= 0.8*X2 + 0.1
0.20m: Y= 1.6*X2 + 0.1
0.25m: Y= 2.4*X2 + 0.1
0.30m: Y= 3.2*X2 + 0.1

## Slide 15: Mesh for Routlet = 0.30m

## Slide 16: Values of Routlet vs Mach # of Axis & Wall
Routlet =.15m
Axis: mach 2.05, Wall: mach 2.55
Routlet =.20m
Axis: mach 2.3, Wall: mach 3.55
Routlet =.25m
Axis: mach 2.5, Wall: mach 4.45
Routlet =.30m
Axis: mach 2.55, Wall: mach 5.25

## Slide 17: Graph of Routlet vs Mach # of Axis & Wall
Wall
Axis

## Slide 18: Conclusions
For the given geometry, we see a linear relationship between mach # & outlet radius at the wall, but the increase in axis mach number diminishes as the outlet radius increases.
Should try different nozzle shapes to see if higher mach numbers for a given expansion ratio can be achieved, possibly convex, or a mix of concave(current shape) and convex
Could also do a study of the range of acceptable back pressures for the different nozzle geometries